| SAFETY | SOSO | Current Issue: 06/13/03 Revision: 4 By: P. Daigle |
| --- | --- | --- |
| Verified by:___ Date:_________ | Entry to Top of Tankage and Upper Levels of Towers |  |
| Date Reviewed: 01/13/20 | I-D-02.10 Page 1 of 1 | Original Issue: 1/5/95 Originator: P. Daigle |

STATEMENT OF PROCEDURE:

The purpose of this procedure is to control access to upper areas of storage tanks and towers in the plant.  Towers referred to by this procedure are the Recovery Column, Heads Column, Product Column and AOGI Stacks.  This procedure takes affect when anyone needs to go up a tower above the top deck of purification level or on to a tank.  Many tanks in the plant have floating roofs with atmospheric vents to facilitate travel of the floating roof.  During tank filling operations there is the possibility of vapors being emitted from the atmospheric vents.  Permission to access upper areas of storage tanks and towers must be obtained from personnel responsible for the area.  Requiring this will greatly reduce search area in the event of an emergency condition.

The contents of this procedure meets all requirements of the Ineos 20 Principles for Behavioral Safety and Process Safety Management as detailed in SOSO I-A-01.06.

PROCEDURE:

1.	Before using a stair or ladder to access upper areas of any tank in the plant, permission must be obtained from the personnel responsible for the area.  The reason for entry must be discussed and any safety precautions agreed to prior to permission being granted.  If a job order is involved the full scope of the work must be discussed.

2.	One or more of the persons accessing tank tops must have a plant radio.  Radio communication must be maintained with check in just prior to going up on the tank or and immediately after descending the tank.

3.	Personnel from the area in which the tank or tower is located must notify someone from their area that they are going up on a tank or tower.

4.	Work groups building scaffolding or using JLG lifts or other equipment to access heights around tank roofs or tank vents must obtain permission prior to beginning such work.  Once again the full scope of the job must be communicated and safety equipment agreed to prior to permission being granted.

5.	Personnel entering areas referred to by this procedure are required to take an emergency escape pack with them whenever they go into the areas described in the statement of procedure.  Note:  An exception to item 5 is shutdown activities.  After the equipment (tanks, towers) have been cleared for entry, emergency escape packs are not necessary.