| SAFETY | SOSO | Current Issue: 10/18/12 Revision: 11 By: P. Daigle |
| --- | --- | --- |
| Verified by:___ Date:_________ | SPECIAL HOT WORK PERMIT PROCEDURES |  |
| Date Reviewed: 01/13/20 | I-D-05.20 Page 1 of 2 | Original Issue: 03/22/82 Originator: Pat Daigle |

STATEMENT OF PROCEDURE:

A Special Hot Work Permit is required when the normal hot work procedure cannot be followed.  The special permit form is the same form that is used for normal hot work.

The contents of this procedure meets all requirements of the Ineos 20 Principles for Behavioral Safety and Process Safety Management as detailed in SOSO I-A-01.06.

REFERENCES

SOSO I-D-05.10, “Hot Work/Confined Space Entry

SOSO I-D-18.00 Hot Tap Procedure

SOSO I-D-03.00 Lockout Electrical and Mechanical

PROCEDURE

The following defines those conditions that require a Special Hot Work Permit, and the procedure that must be employed prior to issuing such a permit.

1.	Definition:

The following are general classes of work requiring a Special Hot Work Permit:

a.	On hot work to be performed on piping or vessels that cannot be isolated and/or decontaminated.  Some examples are:

1.	Job where a double block valves with a bleeder in between is used for isolation. (The block valves must be chained and locked closed.)

2.	Jobs where temporary plugs are used.

3.	Jobs where blanking is impractical.

b.	On any work requiring "hot taps".  Hot taps are limited to vessels or lines containing water, nitrogen, or steam.  Before proceeding with Hot Taps SOSO I-D-18.00 must be adhered to.

On an exception basis the Manufacturing Manager may grant approval where the vessel or line contains other material.

2.	Definition of Responsibilities:

In addition to the responsibilities as defined in SOSO I-D-05.10 the following shall be included prior to the issue of a Special Hot Work Permit.

a.	The shift manager of the area where the special hot work will be performed must field verify the isolation. This means walking out all piping associated with the work to determine energy sources involved an isolation points.

b.	The Area Manager of the area involved will make sure a detailed check of the proposed work and work site has been done to ascertain what preparations are adequate for the safe performance of the work.  He/she will sign the permit.  He/she will determine sign off responsibilities for the permit.  To be included in box marked other, if he/she deems necessary.

c.	A Maintenance Specialist shall be advised of the work to be performed, and will sign the permit.

d.	The SHE Department must be advised of the work to be performed and okay it prior to the permit being issued.

e.	The area technician must be present for any first break of a system involved in the special permit.

3.	Necessary Preparation for Work:

When issuing a Special Hot Work Permit it will be the responsibility of those who sign the permit to make sure that all necessary safety precautions have been taken including applicable items defined in SOSO I-D-05.10.