| SAFETY | SOSO | Current Issue: 08/09/06 Revision: 2 By: P. Daigle |
| --- | --- | --- |
| Verified by:___ Date:_________ | ANALYZER HOUSES |  |
| Date Reviewed: 01/13/20 | I-D-05.41 Page 1 of 2 | Original Issue: 08/08/03 Originator: L. Hensley |

###### REFERENCED PROCEDURES

I&E Procedure 21.07.31 – Analyzer House Monitor Systems and Calibration

SOSO I-D-05.40 Protection From Oxygen Deficient Atmospheres

SOSO I-D-05.12 Permit to Work

The contents of this procedure meets all requirements of the Ineos 20 Principles for Behavioral Safety and Process Safety Management as detailed in SOSO I-A-01.06.

###### STATEMENT OF PROCEDURE

Analyzer Houses:

Analyzer Houses pose an attractive hazard at our facility.  They are climate controlled so they are inviting places to warm up or cool down.  Many of the pieces of equipment have instrument air connected to them.  Since instrument air can be backed-up by nitrogen the possibility of an oxygen deficient atmosphere exists.  To combat this hazard the following conditions must be met.

a.)	All analyzer houses must be locked.  Non-routine entry must be approved by the on duty shift manager or step-up supervisor.  Non-routine would include making repairs to malfunctioning detectors.  Routine entry (i.e. I&E and Production, need only notify the area board technician prior to entry.

b.)	All analyzer houses must have an emergency key located in a tamper proof box near the access door to the house.

c.)	All analyzer houses must have signage designating the asphyxiation hazard

d.)	All analyzer houses must have an Oxygen detector and other detectors appropriate for the hazards present.  Detectors are to have high audible and visible local alarms.  If the oxygen detector is out of service for any reason, entry into the analyzer house requires a permit to work and carrying a personal O2 gas monitor.

e.)	All analyzer houses will have power loss shutdowns for Instrument Air and nitrogen lines going into the building.

#### END OF PROCEDURE

| SOSO |  |
| --- | --- |
| General Procedures |
| ID0541 Analyzer House |
|  | 111119 | Alarms |
|  |  | Oxygen and other atmospheric detectors in the analyzer houses must have either a high audible or a visible local alarm. |
|  |  | A. True |
|  |  | (B.) False |
|  | 111120 | Routine Maintenance |
|  |  | For routine maintenance in the analyzer house, you need only to notify the board technician for that area. |
|  |  | (A.) True |
|  |  | B. False |