| Safety | SOSO | Date Reviewed: 05/26/21 Revision: 12 By: P. Daigle |
| --- | --- | --- |
| Date Printed: ________________ | Barricades, Guards, and Roping Off |  |
| Initials: _________________ |  |  |
|  | I-D-06.00 Page 1 of 5 | Original Issue: 01/27/84 Originator: P. Daigle |

STATEMENT OF PROCEDURE:

The installation of a barrier of some appropriate type around a temporary hazard is basic to any good safety program and should be erected immediately after the hazard is discovered, or prior to starting a task where exposure(s) to personnel safety will be created or are likely to occur.  The area affected will be inspected to determine the extent of barricading and the type of barricade tape required.  The barricade must be placed as to guard all access routes to the hazard.  The erection of the barrier should be reported to and approved by the supervisor of the affected area.  Should you need further assistance contact the Ineos Safety Department as soon as possible.

Barricade tape will not be used for any purpose other than barricading.  Care must be taken to only barricade the area that needs to be closed to access; temporary stands should be used as necessary.  When the hazards no longer exist, the barricade must be removed.  If safety equipment is to be enclosed within a barricade, consideration should be given to providing auxiliary equipment.

All barricades should be labeled on all sides stating the reason why erected (the hazard), date erected, responsible party and if required, all Personal Protective Equipment PPE required for entering the barricaded area.

The contents of this procedure meets all requirements of the Ineos 20 Principles for Behavioral Safety and Process Safety Management as detailed in SHE Policy I-A-01.06.

SHE Policy I-D-00.50  Stop Work Intervention

SHE Policy I-F-01.91 Scaffolding and Elevated Work

PROCEDURE:

1.	When manhole covers, platform sections, valve pit covers, floor openings created (hole > 12”) stairs, vertical ladders, or handrails must be removed:

a.	Properly GUARD the exposed opening.  The materials selected must be strong enough (i.e.  Rigid wood, metal) to prevent personnel from accidentally falling into an unexpected opening.

b.	Hang barricade tags on the barricade at all sides stating why the barricade has been put in place, who erected it and the date it was erected, all PPE required for entering barricaded area.

2.	Excavations that create a hazardous uneven walking surface or constitute a confined space shall be barricaded.  The materials selected for use as a barricade must be plainly visible and "strong enough" to prevent personnel from accidentally falling into the excavation, (i.e. rigid wood, metal).

a.	Hang barricade tags from the barricade at several locations stating why the barricade has been put in place (the hazards), who erected it and the date it was erected, all PPE required for entering barricaded area.

b.	The barricade must be erected at a distance far enough away from the opening as to prevent someone from falling into the opening if the barricade is accidently breached.

3.	Follow the below guarding requirements when a leak is suspected or exists, maintenance work is taking place in or above a traffic area, a load is being lifted or suspended from a crane, hydrotesting, x-ray or other hazards exist.

a.	Properly barricade the entire area affected with the properly colored barricade tape.  If the hazard warrants, use two rows of barricade tape. Support one row of tape at waist level and the second row at shoulder level.  Nighttime illumination is needed for areas where there is a reasonable possibility of someone entering a barricaded area and being harmed due to the inability of recognizing the barricade.

b.	Hang barricade tags from the barricade on all sides stating why the barricade has erected, when it was installed and who installed it, all PPE required for entering barricaded area.

4.	We will be utilizing several different types of barricade tape for different situations:

I.	Yellow "Caution" tape – Will be used when the hazard(s) are apparent to the individual entering the area and the risk is low.  Caution must be used when entering the barricaded area.  Personnel should walk around if possible or, if you must enter the area be alert to the hazard and take precautions to prevent injury.

Some examples of “Low Risk Hazards” are tripping hazards, a leak that is not toxic or flammable, low hanging pipe or scaffolding.

II.	Red barricade tape – Will be used when the risk is high or the hazard is not apparent to passersby.  Red barricade tape is used when an area should not be entered without appropriate PPE or without proper work group approval due to the severity of conditions inside the area.

The work group or work groups working that area must approve all entry into areas with red barricade tape.  If no work group is present check with Production before entering the barricaded area.  Red barricade tape has the wording "Danger Do Not Enter" for additional emphasis.  At the time the area is barricaded all unnecessary personnel must be removed from the area.  Careful attention must be made in notifying all personnel in the area that may be affected by the barricade.

Some examples of “High Risk Hazards” are, a leak that is toxic, flammable or otherwise hazardous, when work activities allow or may allow the release of potentially hazardous contaminants, overhead lifts utilizing cranes or other equipment (the area within the swing radius of the load and counter weights should be barricaded – see section 6 for more information on barricading for cranes), equipment which has partially failed, and could suddenly fail, and continues to operate, activities requiring breathing air, overhead work in which objects could fall.

Operations MUST approve the use of red barricade.

III.	Yellow with Purple Stripe tape - This is used in areas where x-ray is in use and the area should not be entered.

4.	When X-ray work is in progress very SPECIFIC "barricade" procedures MUST BE IMPLEMENTED.  Special signs depicting the radiation symbol, the Universal Propeller, shall be displayed on all sides of the purple and yellow barricade.  Plan this type of operation with the Supervisor.

5.	Only the work group that installed the barricade can modify the barricade (i.e. reduce).

6.	Barricading for Cranes – Crossing a red barricade during a crane lift without permission from those who installed the barricade is a violation of Ineos Life Saving Rules.  Violation of this Life Saving Rules.will result in immediate removal of the offender(s) from the plant site.

Red barricade is only required when there is tension on the load and/or an actual lift is being made.  Every effort should be made to remove red barricade when no lift is occurring.  It can be left up if intermittent lifts will be done during the course of the shift.

7.	Proper Erection of Barricade - Many times workers will use existing equipment and 	structure to secure the red barricade used to demarcate the lift radius.  This can cause 	the lift radius to be much larger than really necessary, blocking Operation’s access to 	equipment.  Therefore, workers should use cones to secure the red barricade in order 	to properly mark the lift radius.  The marking of the lift radius will be discussed during 	the Permit to Work process.

8.	When vehicle restriction is necessary, barrier ropes or wooden barricades mounted on sawhorses should be used.

a.	Hang barricade tags from the barricade on all sides stating why the barricade has been put in place, when it was installed and who installed it.

9.	It is the responsibility of all plant personnel to honor the intent of this SHE Policy.

10.	It is important that all barricades and temporary guards be removed when the job is complete.  Respect for these temporary safeguards can be jeopardized if they are allowed to remain in place longer than the task and/or hazard requires.  The work group that installed the barricade is responsible for removing it.

Questions:

| SOSO |  |
| --- | --- |
| General Procedures |
| ID0600 Barricades, Guards, & Roping Off |
|  | 111114 | Barricading |
|  |  | When manhole covers, platform sections, valve pit covers, stairs, vertical ladders, or handrails must be removed, which two steps must be followed? Check All That Apply: |
|  |  | _X_ Properly guard the exposed opening. |
|  |  | ___ Place red barricade tape around opening. |
|  |  | _X_ Hang "notice" sign or "danger" signs from barricades at several locations stating why the barricade is in place. |
|  |  | ___ Notify safety department of the exposed opening. |
|  | 111115 | X-Raying |
|  |  | When x-raying is taking place, the area affected should be barricade taped off and notice given to prevent access to the area. |
|  |  | (A.) True |
|  |  | B. False |
|  | 111116 | Yellow Caution Tape |
|  |  | Yellow caution tape indicates the following: |
|  |  | (A.) Appropriate additional PPE must be worn to enter taped area. |
|  |  | (B.) Extreme caution must be used when entering the area. |
|  |  | C. Rubber boots and coveralls are required to enter taped area. |
|  |  | D. X-Ray is taking place in the area. |
|  | 111117 | Barricade Tags |
|  |  | Barricade tags stating the purpose of the barricade should only be placed on the north and south sides of the barricade. |
|  |  | A. True |
|  |  | (B.) False |
|  | 111118 | Temporary Guards |
|  |  | Temporary guards or barricades should be removed at what point? |
|  |  | (A.) At the completion of the job. |
|  |  | B. When they get in the way of other work. |
|  |  | C. At shift change. |

| APPROVALS: | DATE: |
| --- | --- |
| Chris Urbanowich – SHE Mgr. | 05/14/21 |
| Pat Daigle – Safety Specialist | 05/14/21 |

LOG OF CHANGES AND REVISIONS:

| Revision# | Date | Mod B# | Revision |
| --- | --- | --- | --- |
| 12 | 05/26/21 | 18964 | Removed orange barricade for coverall required |