| Green Lake Site | SHE Asbestos-Containing Material Handling Practices Criticality: 3 Review Date: 06/26/23 Page 1 of 2 | I-D-09.60 Revision: #03 Revision Date: 06/26/23 Owner: C. Urbanowich |
| --- | --- | --- |

STATEMENT OF PROCEDURE:

This procedure outlines the health and safety requirements for the removal of Asbestos Containing Material (ACM) or Presumed Asbestos Containing Material (PACM). Asbestos is a mineral that readily separates into long flexible fibers suitable for use as a noncombustible, non-conducting or chemically resistant material.

While Green Lake no longer purchases ACM, there have been several areas identified that may contain asbestos material:

o	Laboratory analysis shows 2% asbestos in the black mastic under the floor tiles.

o	There is a possibility that several vehicles contain asbestos brake pads and clutches.

o	Panels in Laboratory hoods.

The contents of this procedure meets all requirements of the Ineos 20 Principles for Behavioral Safety and Process Safety Management as detailed in SOSO I-A-01.06.

# OBJECTIVE

The recommendations contained in this procedure are intended to minimize exposure to Asbestos in the workplace and to meet the requirements mandated by OSHA standards 1910.1001 and 1926.1101.

Procedure recommendations shall be followed during the following types of activities:

1.	Repair or renovation on structures where floor tiles are disturbed.

2.	Maintenance guideline 14.4 "Removal, Installation and Disposal of Brake Pads and Clutch" will be followed for removal and disposal of brake pads and clutches.

3.	Disturbance of panels in Laboratory Hoods.

# PROCEDURE

An approved asbestos abatement contractor will be used whenever repair or renovation on structures where floor tiles are to be disturbed. Asbestos-containing material shall only be handled, removed, cut, scored, patched, taped, or otherwise worked on by appropriately certified asbestos abatement contractors. The only exception to this is the removal of brake pads and clutches which is outlined in Maintenance Guideline 14.4. The certified contractor will comply with all applicable Federal, State and Local regulations including, but not limited to OSHA's Asbestos Standard 29 CFR 1910.1001 - 1926.1101.

# MONITORING

Asbestos abatement contractor will be responsible for conducting exposure monitoring and ensuing adequate personal protection equipment is worn and exposures are below the PEL.

# EXPOSURE LIMITS

PEL 0.1 f/cc

Reviewer’s Approval

| Name | Title | Date |
| --- | --- | --- |
| Chris Urbanowich | HSEQ Manager | 06/07/23 |

Document Change History

| Revision Date | Version Number | MODB Number | Description of Change | Author |
| --- | --- | --- | --- | --- |
| 06/26/23 | 3 | 19701 | Reviewed with no revisions, 2022 Personal Safety Commitment Administrative/Format Updates: Pg. #1 Header, “Reviewer Approval”, and “Document Change History” updated to QPGL400, removed VTA questions, and added statement in Footer. | D. Maroney |