| SAFETY | SOSO | Date Reviewed: 12/08/22 Revision: 5 By: J. Moss |
| --- | --- | --- |
| Date Printed: _________________ | Work Over Water |  |
| Initials: _________________ |  |  |
|  | I-D-11.50 Page 1 of 3 | Original Issue: 07/18/91 Originator: P. Daigle |

STATEMENT OF PROCEDURE

Occasionally jobs come up in the facility that require personnel to work over bodies of water.  Water can present unique hazards such as the possibility of drowning or of electrical shock.  This procedure attempts to outline certain precautions that are to be taken when working over bodies of water.  Each job presents unique problems so thought must be given to any additional hazards that may be present.  The permit to work process should be used to insure hazards are adequately addressed.

The contents of this procedure meets all requirements of the Ineos 20 Principles for Behavioral Safety and Process Safety Management as detailed in SOSO I-A-01.06.

REFERENCES

SOSO I-D-05.12 Permit to Work

SOSO I-F-01.90 Personal Fall Protection Equipment

SOSO I-F-01.91 Scaffolding and Elevated Work Procedures

PROCEDURE

Definition of work over water - Any task that must be completed outside of permanently installed walkways or platforms over a body of water three (3) feet deep or deeper.

1.	To board any floating vessel Coast Guard approved personal floatation devices must be worn.  Personal floatation devices must be inspected prior to each use for dry rot, chemical damage or other defects which may affect their strength or buoyancy.

2.	For any jobs requiring personnel to work on unguarded (not completely enclosed by side and midrails) platforms five (5) feet or more above a body of water; fall protection is required.  Guarding is preferred but where impractical, safety nets or safety belts and lifelines are mandatory.  100% tie-off must be followed at all times.  A personal flotation device must be worn when accessing ladders where 100% tie-off cannot be used.

3.	In the vicinity of each worksite over a body of water three (3) feet or deeper there must be at least one portable or permanent ladder of sufficient length to assist employees to reach safety in the event that they fall into the water.  Whenever possible this ladder should be installed at water level prior to beginning work on the job in question.

4.	At least one life ring with a line attached shall be located at the job site within 50 feet of where the work over water is taking place.

5.	A stretcher with permanently equipped bridles for hoisting must also be at the job site where work over water is being performed.

| SOSO |  |
| --- | --- |
| General Procedures |
| ID1150 Work Over Water |
|  | 111352 | Permit to Work Purpose |
|  |  | What permit is used to insure hazards are adequately addressed when working over water? |
|  |  | A. Hot Work |
|  |  | (B.) Permit to Work |
|  |  | C. Prequalification |
|  |  | D. New and Unusual Job |
|  | 111353 | Applicable Areas |
|  |  | The Work Over Water procedure applies to all work outside permanently installed walkways or platforms and the water where the water is 35 inches deep. |
|  |  | A. True |
|  |  | (B.) False |
|  | 111354 | PPE for Floating Vessels |
|  |  | What PPE must be worn to board a floating vessel? |
|  |  | A. Coast Guard approved flotation device |
|  |  | B. Flame Retardant Clothing |
|  |  | C. Hard Hat |
|  |  | D. Safety Glasses |
|  |  | (E.) All of the above |
|  | 111355 | Fall Protection |
|  |  | You must wear and use 100% fall protection on unguarded platforms five feet or higher above water. |
|  |  | (A.) True |
|  |  | B. False |
|  | 111356 | Special Equipment |
|  |  | What items are required to be at the work area while conducting work over water? Check All That Apply: |
|  |  | _X_ one throwable life ring |
|  |  | _X_ ladder |
|  |  | _X_ stretcher |
|  |  | ___ supervisor |

| APPROVALS: | DATE: |
| --- | --- |
| Chris Urbanowich – SHE Mgr. | 10/17/22 |
| Jacob Chambless – Safety Specialist | 10/17/22 |

LOG OF CHANGES AND REVISIONS:

| Revision# | Date | Mod B# | Revision |
| --- | --- | --- | --- |
| 5 | 12/08/22 | 19417 | Reviewed with no revisions, 2022 Safety Commitment |