Contents

1	IN-PLANT Vehicular Transportation Overview	1

1.1	Statement of Procedure	1

2	Procedure	2

2.1	Procedure	2

3	Document List	4

4	Change Log	4

# IN-PLANT Vehicular Transportation Overview

## Statement of Procedure

### To provide a procedure for plant personnel who are transported by vehicles, inside the location boundaries, while on duty.

### This procedure will apply to all vehicles and industrial mobile equipment driven in the plant by the Green Lake Complex and contractor personnel.  Additional information regarding company vehicle use can be found in SPAG–E-8.

### The contents of this procedure meets all requirements of the Ineos 20 Principles for Behavioral Safety and Process Safety Management as detailed in SOSO I-A-01.06.

# Procedure

## Procedure

### The operator of any vehicle within the boundaries of the Green Lake Plant is completely responsible for safe operation of the vehicle and compliance with all safety procedures related to vehicular operation.  No cellular calls will be made or received (this includes hands-free calls), while driving on company business, by employees in the Nitriles BU and you must stop and pull over to read a text message.

### A 360° walk around will be conducted by the driver prior to backing up any vehicle into any process unit on the west side of the railroad tracks.

### This is not a requirement for backing into a designated parking spot. A designated parking spot has clearly indicated / painted lines on the pavement. A 360° walk around will be conducted by the driver (or alternately, the spotter) prior to driving into or out of a congested area. Sound the vehicle’s horn just prior to driving in reverse to alert others of the vehicle’s movement.

### All vehicles or mobile equipment require an adequate number of spotters when backing in the operating unit of the plant.

### Seatbelts need to be installed and worn in all vehicles with roll-over protection.

### Use of plant radios while driving is prohibited unless it is during an emergency situation or response.

### All loads transported in the vehicle must be secure and not exceed the manufacturers design specification for the vehicle.

#### Loads will not extend more than four feet to the rear or six inches to either side. Any load extending beyond the vehicle sides or more than 12 inches to the rear will be flagged.

### The number of passengers in a vehicle should not exceed the number of seatbelts provided by the manufacturer.

### All operators of industrial mobile equipment must be trained and medically fit to operate the vehicle.  Refer to the equipment specific SOSOs for more information on training and certification requirements such as I-D-10.00 Lifting Safety regarding the operation of cranes.

### The operator will obey all posted speed limits and traffic signs.

### The driver of a vehicle shall never leave the vehicle while the engine is running unless the wheels are chocked.

### Seat belts must be worn by drivers and passengers where provided.  This includes all mobile equipment provided with overhead protection.  Disabling seatbelt protection violates Life Saving Rule #4 Safety critical devices/interlocks must not be disabled or overridden without authorization.

### Personnel must be seated inside the vehicle and shall not be supported by the bumper, running board, tail gate, or any part of the vehicle not designated to carry people.  Standing in a moving vehicle is absolutely forbidden.  The keys must be left in the ignition of unattended vehicles on the west side of railroad tracks for emergency response purposes.

### Riding in back of trucks is not allowed.

### All heavy or bulky loads shall be secured to the truck bed to prevent movement while in transit.

### Securing of loads shall be accomplished by utilizing approved rigging techniques and equipment.

### Annual PMs will be conducted on all plant vehicles.

### A pre-use visual inspection will be conducted by plant personnel prior to operating a plant vehicle.

### All in-plant vehicular traffic should be looking out for bicycles and pedestrians especially at night.  Vehicles driven at night must have headlights on.

### All traffic including vehicle and pedestrians must yield right of way to large industrial equipment such as; manlifts, forklifts, cranes, backhoes, etc.

# Document List

Table 1: Document Reference List

| Title | Location |
| --- | --- |

# Change Log

Review History

Table 2: Review History

| Description | Document and Data Control |
| --- | --- |
| Last Review Date | 03/07/24 |
| Last Review By | C. Urbanowich |
| Next Review Due Date | 03/06/27 |

Reviewer’s Approval

Table 3: Reviewer’s Approval

| Name | Title | Date |
| --- | --- | --- |
| Chris Urbanowich | HSEQ Manager | 03/07/24 |
| Willishia Rudd | SHE Training Specialist | 03/07/24 |
| Jose Rodriguez | Operations Manager | 03/07/24 |

Document Change History

Table 4: Document Change History

| Revision Date | Version Number | MODB Number | Description of Change | Author |
| --- | --- | --- | --- | --- |
| 10/29/20 | 16 | 18502 | Removed riding in back of trucks. Added yielding to large industrial vehicles. | P. Daigle |
| 05/26/21 | 17 | 18965 | Pg. #1: Added 6a, completed by the BBS Team as a result of BBS observation data. Added requirement to flag loads that extend outside vehicles. BBS Team members Kriston Wachtendorf and Scott Babb | D. Har-Even |
| 03/12/24 | 18 | 20207 | Pg. #2: Revised step 2.1.2 and created step 2.1.3 to clarify conducting a 360 walk around is not required when backing a vehicle into a designated parking spot. New procedure format. | C. Urbanowich |