| SAFETY | SOSO | Current Issue: 02/12/20 Revision: 10 By: P. Daigle |
| --- | --- | --- |
| Verified by:___ Date:_________ | INSPECTION AND COLOR CODING OF EQUIPMENT |  |
| Date Reviewed: 02/12/20 | I-E-00.01 Page 1 of 6 | Original Issue: 06/25/90 Originator: P. R. Daigle |

###### STATEMENT OF PROCEDURE

Various equipment used in the unit must be serviceable in order to be used safely.  Therefore, periodic inspections are a must.  The purpose of this procedure is to give guidance on proper storage and identification of equipment, establish inspection periods and responsibilities and provide color coding guidelines for equipment.

The contents of this procedure meets all requirements of the Ineos 20 Principles for Behavioral Safety and Process Safety Management as detailed in SOSO I-A-01.06.

PROCEDURE

Part I

1.	Equipment covered in Part I includes portable electric tools and extension cords, ladders, rigging, safety belts, safety harnesses and lanyards.

2.	Each department must label all its “equipment” with a unique identifying number.  A copy of each department’s list of equipment is to be sent to the Safety Department for inspection purposes.

3.	Each department will identify and label the proper storage area for each piece of equipment.  After each use, equipment is to be returned to its proper storage area.

4.	The Safety Department will be responsible for inspecting and color coding of ladders, and safety equipment during the last two weeks of each quarter for the upcoming quarter.  As a result, at the end of each quarter, workers will be using equipment that has the color code for the upcoming quarter.  The Safety Department is responsible for inspecting rigging.  I&E will be responsible for completing the quarterly inspection, testing, and color coding of portable electric tools and extension cords in accordance with SOSO I-E-04.10.

5.	Quarterly color codes are as follows:

| 1st Quarter | Blue | Jan Feb Mar |
| --- | --- | --- |
| 2nd Quarter | Green | Apr May June |
| 3rd Quarter | Red | Jul Aug Sep |
| 4th Quarter | Orange | Oct Nov Dec |

6.	Any equipment that shows signs of damage, is to be tagged “Do Not Operate”.  Work orders are to be written for proper repair or disposal of damaged equipment.

7.	Code for Equipment Identification

AREAS

| BD | Barge Dock |
| --- | --- |
| ACH | ACH |
| PN | Purification |
| RR | Rail Rack |
| CBI | CBI |
| #1 Rx | #1 Rx |
| #2 Rx | #2 Rx |
| ANC | AN Control |
| UT | Utilities |
| I&E | I&E |
| PM | Plant Maintenance |

EQUIPMENT

| L | Ladders |
| --- | --- |
| EL | Electrical Tools |
| R | Rigging |
| SB | Safety Belt, Safety Harnesses and Lanyards |

In labeling, the area is designated first, then the equipment code, then the number.  For example ACH L3 designates ACH Ladder #3.  ANC SB1 designates AN Control safety belt #1.

Part II

This section deals specifically with scaffolding.  Scaffolding used in the plant must be inspected by the work group responsible for erecting it.  All scaffolding must conform fully to OSHA Regulations.  Tags will be used to identify the status of the scaffold.  The color code for the scaffold is as follows.

SCAFFOLD INSPECTION TAGS:

| Green Tag | A Green Tag signifies that the scaffold meets all OSHA requirements for scaffold(s) applications. User is not required to wear a harness while working from a green tagged scaffold. |
| --- | --- |
| Yellow Tag | A Yellow Tag signifies that the scaffold has an identified hazard. All yellow tagged scaffolds 4 feet or higher, require: Tie-off while physically on scaffold. |
| Red Tag | This Red Tag signifies the scaffold has a substandard condition that makes it unsafe to use! No-one, except; “Qualified Personnel” (whose sole purpose is to repair and/or modify the scaffold) is allowed onto the scaffold in question. |

Part III

Stationary cord and plug connected equipment and flexible cord sets which remain connected once they are put in place and are not exposed to damage, are to be visually inspected by the installer on initial use and when relocated.

Part IV

This section deals with the color coding of alarms, detectors, and other miscellaneous equipment.

A.	OSHA Alert Orange

- Spill Release Alarms & Backgrounds

- Page Talk Boxes

- Chains on V/V Operators

- Sample Point Markers

B.	OSHA Fire Protection Red

- Fire Alarm Activation Switches & Background

- Fire Extinguishers & Backgrounds

- Fire Hydrants

- Fire Monitors

- Post Indicator Valves (PIV)

- Fire Water Piping, Equipment and Foam Chambers and Piping

C.	OSHA High Visibility Yellow

- Emergency Shutdown Switches & Backgrounds

- Lifesaver Guard Rail Background

- Structure Ladders and Cages

- Overhead Hazards

- Tripping Hazards

- Hose Racks

- Stair Toe Threads

- Derailers at Railrack

- Barricade Posts

D.	OSHA Safety Green

- EBA Background

- Eyewashes

- Hearing Protection Stripes

- Safety Shower Pads

- Oxygen Piping

E.	OSHA Blue

- Ammonia Detectors Background

- Earplug Boxes

F.	OSHA Safety Purple

- Sulfur Dioxide Detectors Background

G.	Fluorescent Green

- HCN Detectors Background

H.	Fluorescent Pink

- Valve wrenches

- Combustible LEL Sensors Background

I.	Utility Drops must have the following color scheme:

- Water	-Blue (Drop Stenciled “H2O”)

- Steam	-Black (Drop Stenciled “Steam”)

- Plant Air	-Red Drop (Drop Stenciled “Plant Air”)

- Nitrogen	-Yellow (Drop Stenciled “N2”)

Part V

Electrical Receptacles:

Electrical receptacles are inspected and tested by the I&E Department on a biannual basis.  These inspections take place in January for the first 6 months and July for the second half of the year.

Color code as follows:

Black Tag:  January – June

Yellow Tag:  July - December

Part VI

Flagging Tape

The flagging colors listed below should only be used for the task listed and for no other purpose.

Pink Flagging:  used to flag blind locations (See I-D-15.00 Blanking procedure).

Lime Green Flagging:  used to mark location of first break (See I-D-05.12, Permit to Work and I-D-04.60, Opening Lines).

#### END OF PROCEDURE

| SOSO |  |
| --- | --- |
| General Equipment |
| IE0001 Inspection & Color Coding Equip |
|  | 111487 | Inspection Colors |
|  |  | I&E uses color coding to indicate the inspection for portable electric tools and extension cords. What quarter is represented by the color RED? |
|  |  | A. 1st Quarter (Jan Feb Mar) |
|  |  | B. 2nd Quarter (Apr May Jun) |
|  |  | (C.) 3rd Quarter (Jul Aug Sep) |
|  |  | D. 4th Quarter (Oct Nov Dec) |
|  | 111488 | Damaged Equipment |
|  |  | Any equipment that shows signs of damage is to be tagged ________ . Work orders are to be written for proper repair or disposal of damaged equipment. |
|  |  | A. Broken |
|  |  | B. Damaged |
|  |  | (C.) Do Not Operate |
|  |  | D. Throw Away |
|  | 111489 | Equipment Labeling |
|  |  | In labeling of equipment each department will identify it with a unique number. In this example "ACH L3" designates _______ . |
|  |  | A. Acrylo Ladder 3 |
|  |  | B. ACH Electrical Tools 3 |
|  |  | (C.) ACH Ladder 3 |
|  |  | D. CBI Rigging |
|  | 111490 | Scaffolding Tags |
|  |  | A _________ tag on a scaffold signifies it has an identified hazard, but can still be used. |
|  |  | A. Green |
|  |  | (B.) Yellow |
|  |  | C. Red |
|  |  | D. Blue |
|  | 111491 | Cord and Plug Connections |
|  |  | Stationary cord and plug connected equipment and flexible cord sets, which remain connected once they are put in place and are not exposed to damage, are to be visually inspected by the installer __________ . |
|  |  | A. weekly |
|  |  | (B.) on initial use and when relocated |
|  |  | C. annually |
|  |  | D. semi-annually |
|  | 111492 | OSHA Alert Orange |
|  |  | Which of the following is not color coded OSHA Alert Orange? |
|  |  | A. Spill Release Alarms and Backgrounds |
|  |  | B. Page Talk Boxes |
|  |  | (C.) Fire Hydrants |
|  |  | D. Chains on V/V Operators |
|  | 111493 | Electrical Receptacles |
|  |  | Electrical receptacles are inspected and tested by the I&E Department on a biannual basis and are color coded Black and Yellow. Which months are indicated by the color Yellow? |
|  |  | A. January - June |
|  |  | (B.) July - December |