| SAFETY | SOSO | Current Issue: 07/24/18 Revision: 4 By: P. Daigle |
| --- | --- | --- |
| Verified by:___ Date:_________ | SAFE SLING OPERATION |  |
| Date Reviewed: 07/24/18 | I-E-07.00 Page 1 of 3 | Original Issue: 08/20/02 Originator: P. Daigle |

###### STATEMENT OF PROCEDURE

The purpose of this procedure is to promote the safe use of slings throughout the plant.  Reference the Maintenance Guideline for specific information on the different types and use of slings.

The contents of this procedure meets all requirements of the Ineos 20 Principles for Behavioral Safety and Process Safety Management as detailed in SOSO I-A-01.06.

Scope:

  - General Requirements

  - Identification and Inspection

  - Repairs

Responsibility:

It is the responsibility of all site personnel associated with the use and distribution of slings, to know and understand the contents of this procedure.  Only employees qualified and trained on proper rigging methods per 29 CFR 1926 Cranes and Derricks in Construction should use slings.

PROCEDURE

Method:

- General Requirements

  - No sling shall be used in excess of the rated capacity.

  - No sling shall be used in a manner that will change its rated capacity, i.e., double choking 2 slings; lifting with excessive angles.

  - Slings shall be stored in a dry, well-ventilated area and lubricated to prevent corrosion.

  - Proper rigging methods will be used to prevent damaging slings when lifting objects. Attachments (shackles, lifting eyes or other approved lifting attachments) will be used between the object being lifted and the slings whenever necessary to prevent damaging slings. Wire rope slings will not be eye choked (cable eye crimp passes back through same eye of the choker), choked around sharp objects without using a protector or used in a manner that will render the sling unserviceable.

  - Alloy chain and metal mesh slings will only be used on special approved applications. The use of alloy chain and metal mesh slings, for routine rigging, applications is prohibited.

- Identification and Inspection

## All alloy steel chain slings shall have a permanently affixed durable identification stating size, grade of material, rated capacity, and reach.

## All synthetic web slings shall have a permanently affixed durable identification stating the material, size, and load rating.

## Inspections

### Before initial use, each new sling shall be inspected to determine that it is free of defects. The manufacturer will supply a Certificate of Proof Test on applicable slings. The Certificate of Proof test will be readily available to the Green Lake Facility site personnel upon request.  The Rigging Department will maintain the Certificate of Proof test for all slings belonging to the site.

### Slings will be inspected prior to use, to determine that it meets the job requirements and is free of defects and damage. Any fastenings and attachments used in conjunction with a sling must also be inspected for defects or damage.  When a condition is presented that would require the sling to be removed from service it shall be tagged with a “Do Not Operate” tag and immediately removed from service.  Those slings belonging to the site will be taken to the Rigging Department for exchange.

    - Slings belonging to the site will inspected quarterly by the Safety department and color coded according to site guidelines.

## Repairs

  - All damaged or worn slings should be tagged with a “Do Not Operate” tag and taken out of service.  Those slings belonging to the site will be returned to the Rigging Department for replacement and then subsequently destroyed by that department. All non-resident contractors need to promptly remove damaged or worn slings from the plant site.

#### END OF PROCEDURE