| SAFETY | SOSO | Date Reviewed: 12/09/22 Revision: 6 By: J. Lidiak |
| --- | --- | --- |
| Date Reviewed: ________________ | HAND PROTECTION |  |
| Initials: ________________ |  |  |
|  | I-F-01.20 Page 1 of 5 | Original Issue: 02/23/95 Originator: P. R. Daigle |

###### STATEMENT OF PROCEDURE

To establish guidelines for reducing the probability of injury through proper selection, inspection, and care of hand protection based on the job task to be performed.

In no way is it possible to indicate every job task, with every scenario possible that is performed by various work groups.  The information below will give you basic guidelines.

The contents of this procedure meets all requirements of the Ineos 20 Principles for Behavioral Safety and Process Safety Management as detailed in SOSO I-A-01.06.

SELECTION

Glove selection will be based on the job task to be performed, the hazards of the task, and/or the type of injury that could be encountered.  Appropriate hand protection is to be selected for each task.  Listed below are various gloves that are available to you through the Stores Warehouse.  *Ineos Green Lake employees and contractors shall carry a pair of the Posi Grip or leather gloves with them when in work areas of the plant (excludes office and break areas).  This is to ensure the employee has a minimum level of hand protection readily available.

Posi Grip Gloves- This is Ineos Green Lake’s all purpose glove.  It is made of cut resistant engineer yarn gloves that have the polyurethane (PU) palm dip.  The PU palm makes them a good glove for wet or oily tasks.  They are good for any cutting or sharp edge task.  This glove is not suitable if a liquid hazard is present.  The glove is reusable, but must be properly disposed of if contaminated.

*Leather Gloves are advised for most work that could have the potential for injury such as abrasions, cuts or punctures.  They are not suitable if a liquid hazard is present.

*  If a chemical contact occurs while wearing Posi Grip or leather gloves, they must be removed immediately, the area under the glove washed for at least 15 minutes.  Dispose the contaminated glove properly and report to your supervisor and/or seek medical attention if needed.  (Reference specific SOSO or EOP procedures)

Neoprene Gloves are the primary gloves used for sampling at our facility.  They are acceptable for sampling all chemical streams but they must be disposed of whenever any chemical is splashed on them.  Some chemicals will permeate the gloves very quickly.  Therefore we use these neoprene gloves for splash protection only.  They can be used for other light work around chemicals as long as the first splash rule is followed.

PVC Gloves are recommended for heavy work, where there is a higher probability of chemical contact or an increased probability of tearing the glove, involving the chemicals listed in the table.

Butyl Rubber Gloves are recommended for heavy work (as defined under PVC gloves) for the chemicals listed in the table.  The Butyl rubber glove are carried in Stores.  This is also the glove that is used for the Andover and Chemrel suits.

Electrical Gloves are used to protect against electrical shock.  They are required when working on circuits 600 volts and greater.  The gloves must be checked prior to each use for defects and electrical tested every 6 months.

Thermal Gloves are recommended for working with extreme temperatures.  The blue tempshield cryo-gloves kept on the OSE van protect to 160°C (not recommended for high temperature work).  High temperature gloves are used on jobs to protect hands against heat related burns.  Firefighter’s leather gloves will give some protection but for extreme heat (such as Nox-out guns), “ZETEX” special purpose gloves are required.  These gloves are made of heat resistant fibers and can give protection to 1000°F and are available at Stores.

Chemical Resistant Gloves

Below is a list of various chemicals and the proper gloves to be worn if your job duties subject your hands to potential exposure to those chemicals.  If a specific chemical is not listed, please refer to the SDS for proper PPE requirements or contact the Safety Department.

| CHEMICAL | PVC | BUTYL RUBBER | NEOPRENE |
| --- | --- | --- | --- |
| Acetone |  | x |  |
| Ammonia |  | x | x |
| Chlorine |  | x | x |
| Acetonitrile | x | x |  |
| Acrylonitrile |  | x |  |
| Formaldehyde |  | x |  |
| ACH |  | x | x |
| HCN |  | x | x |
| Hydrochloric Acid | x | x | x |
| Sulfuric Acid | x | x | x |
| Caustic | x |  | X |
| Isobutanol |  | x | x |
| Glycolic Acid | x | x | x |
| Phosphoric Acid | x | x | x |
| Acetic Acid | x | x | x |

#### END OF PROCEDURE

| SOSO |  |
| --- | --- |
| Safety Equipment/Personnel Safety |
| IF0120 Hand Protection |
|  | 111521 | Glove Selection |
|  |  | Glove selection is based on _______________ . Check All That Apply: |
|  |  | _X_ the job task to be performed |
|  |  | _X_ the hazards of the task |
|  |  | _X_ the type of injury that could be encountered |
|  |  | ___ the weather |
|  | 111522 | Posi Grip Gloves |
|  |  | Posi Grip gloves are cut resistant. |
|  |  | (A.) True |
|  |  | B. False |
|  | 111523 | Liquid Hazards |
|  |  | __________ and ___________ gloves are not suitable if a liquid hazard is present. Check All That Apply: |
|  |  | _X_ Leather |
|  |  | ___ Thermal |
|  |  | ___ Electrical |
|  |  | _X_ Cotton |
|  | 111524 | Sampling Gloves |
|  |  | Which glove is used primarily for sampling at Green Lake? |
|  |  | A. PVC |
|  |  | (B.) Neoprene |
|  |  | C. Butyl Rubber |
|  |  | D. Leather |
|  | 111525 | Chemical Contact |
|  |  | If a chemical contact occurs while wearing Posi Grip or leather gloves, the gloves must be removed immediately, and the area under the glove should be washed for 15 minutes. What next? |
|  |  | (A.) dispose of the contaminated glove properly, report to your supervisor and/or seek medical attention |
|  |  | B. throw away the glove and return to work |
|  |  | C. send the glove to the Lab for testing and return to work |
|  |  | D. save the gloves in your locker and seek medical attention |
|  | 111526 | Potential Exposure |
|  |  | When your job task has the potential to expose you to Acetone, Acrylo, and/or Formaldehyde, you will use which chemical glove? |
|  |  | A. PVC |
|  |  | B. Neoprene |
|  |  | (C.) Butyl Rubber |

| APPROVALS: | DATE: |
| --- | --- |
| Chris Urbanowich – SHE Mgr. | 10/17/22 |
| Jacob Chambless – Safety Specialist | 10/17/22 |

LOG OF CHANGES AND REVISIONS:

| Revision# | Date | Mod B# | Revision |
| --- | --- | --- | --- |
| 6 | 12/09/22 | 19416 | Minor revisions, 2022 Safety Commitment |